## Slide 1
Dataset Dict:
Stage
State
Action
Reward
Mask
Done
Next State
Definitions
Int stage # Has two stages, switch the two target positions, eliminate the need for environment reset
Array.Float [x, y, rz, xc, yc] # x, y, rz are the end-effector positions (EEP) of robot arm, xc, yc is the position of the cube
Array.Float [x’, y’, rz’] # x’, y’, rz’ are the end-effector position velocities (EEV)
Float reward # Reward is negatively propositional to the distances between cube & EEP times cube & target position
Float mask # Time limit cutoff
Boolean done # Task done or not
Array.Float [x, y, rz, xc, yc] # Next state
Json:
{
  {
  “Stage”: 1,
  “State”: [0.12, 0.34, 0.12, 0.34, 0.82],
  “Action”: [0.12, 0.59, 0.98]
  “Reward”: 900.83
  “Mask”: 1.0
  “Done”: False
  “Next State”: [0.13, 0.34, 0.12, 0.34, 0.82]
  }
  {
  “Stage”: 1,
  “State”: [0.12, 0.34, 0.12, 0.34, 0.82],
  “Action”: [0.12, 0.59, 0.98]
  “Reward”: 900.83
  “Mask”: 1.0
  “Done”: False
  “Next State”: [0.13, 0.34, 0.12, 0.34, 0.82]
  }
  {
  “Stage”: 1,
  “State”: [0.12, 0.34, 0.12, 0.34, 0.82],
  “Action”: [0.12, 0.59, 0.98]
  “Reward”: 900.83
  “Mask”: 1.0
  “Done”: False
  “Next State”: [0.13, 0.34, 0.12, 0.34, 0.82]
  }
  …
}

## Slide 2
Communication with Hardware
Communication
Action([x’, y’, rz’])
80Hz
Write EEP
Read EEP
Robot Arm
APIs
AR Code
Positions
Estimation
30Hz
Read the cube position
FK
IK
Get_state()

## Slide 3
Reward
Calculate Reward
Get_state()
Stage update
Int cur_stage
Get_state()
Int new_stage
update_Stage()
Stage
update_Stage()
get_reward()
Int reward

## Slide 4
Generate Offline dataset
Experts’ Action
Experts
Communication
Dataset update
Prior Dataset
Output
State Update
Calculate Reward
Datasets Buffer
Experts’ Observation
Stage update

## Slide 5
RLPD Train
Generate Offline dataset
Action
Communication
Sample from Offline dataset
Datasets Buffer
Online dataset update
Sample from Online dataset
Prior Dataset
State Update
Reward Update
Online Training